## Slide 1: E-Hack Raspberry PI Surveillance system challenge
Martin Siegbahn, Göran Wik, Jose Romero

## Slide 2: Outline
Intro
Surveillance system (Lab Monitor System, LAMOS)
E-hack setup
The Raspberry Pi sensor node
Challenges

## Slide 3: Intro: RPI@ERicsson?
A lot of test and lab equipment at Ericsson needs to be controlled remotely!
The Raspberry Pi is small, cheap, powerful and versatile!
Raspbian Linux give you a lot of freedom
Raspberry Pi community is (now) big: a lot of useful stuff can be found out there...
And, best of all, you can connect different sensors to it! 

## Slide 4: Surveillance System Lab Monitor system (LAMOS)
T(C)
Central surveillance server
Warnings
Status display
LAMOS

## Slide 5: Surveillance system
Lab room with 24/7 operations
Local private lab LAN
Temperature sensor: 1 reading/minute
Camera: 1 picture every 10th second
Central server node that pings ALL equipment in the lab and collects camera/temperature data
External (from lab-LAN) display node that presents lab status
Low bandwidth needs!

## Slide 6: E-Hack Setup
Switch
Internet
DHCP
Rpi1
“Sensor node”
Model B+
Rpi2
“Central server”
Model 2
Additional Rpis
Status GUI
Status GUI

## Slide 7: Raspberry Pi sensor node
A Raspberry Pi model B+ with:
  RPi 5-Megapixel camera module (350 SEK)
  DS18B20 temperature sensor (70 SEK@ Kjell & Co)
Temp sensor adaptor (connector with 4.7 kΩ resistor)

## Slide 8: RPi sensor node setup
1: (Install SD-card with Raspbian)
2: (Connect Rpi camera and temperature sensor)
3: Boot and configure (“raspi-config”) (login:”pi”, passwd:“raspberry”)
  Expand file system
  Enable SSH
  Change keyboard layout, (“HP Internet Keyboard”, Swedish)
  Set locale/time-zone
  Enable camera
  NOTE! Before connecting to internet: change password! (“passwd”, “EHackPi123#”)
  Install FTP (and VNC if you like)
4: Test temp sensor and camera
5: Hack on challenges!

## Slide 9: Challenges Summary
Sensor node: Improved SW for reading temperature.
Server node: Central server that pings all equipment on the local private LAN and collects all sensor data. Puts the results into a record of some kind that can be distributed easily.
Status display node: A simple GUI that presents the lab status.
Configuration: Ansible playbook configuration of all Rpis

## Slide 10: Sensor node challenge
Improved SW for reading temperature.
  It needs to read the temperature at exact intervals, no slip in time!
  Output to simple text log file
  Synchronized from LAMOS central server
SW for taking still pictures with Rpi camera at specified intervals and synchronized from central server node

## Slide 11: server node challenge
Input:
  1) list of ip-address (for nodes to ping and sensor nodes)
  2) Sensor node configuration, time interval etc
Pings all nodes in the lab
Collect all sensor data
Output: a record with all data with time stamp
(Synchronizes the sensor nodes)

## Slide 12: Status GUI challenge
Get sensor record from central server and display it, in a ”nice” way!
  A map of the lab
  Temperatur plots
  Camera picture
Possibility to enable and configure warning-messages
  Input e-mail address where warnings are sent to
  The GUI sends warnings if two criteria are fulfilled
    One node is not responding to ping
    Over-temperature if T>30 deg
An App?

## Slide 13: Configuration Challenge
Configure all sensor nodes with ONE Ansible playbook
Write a playbook to automatically configure the Raspbian

## Slide 15: RPI Components at Kjell & Co
Description | Kjell & Co art no | Price (SEK)
Raspberry Pi 2 model B | 87830 | 399
Plastic case, black | 87275 | 99
Micro SD-kort, 8 GB | 95979 | 170
USB-charger 1A w cable | 94901 | 150
USB-charger 2A w/o cable | 94911 | 150
Micro USB cable, 1.8 m | 68688 | 120
DVI-HDMI-cable | 68096 | 160
DVI/HDMI-adaptor | 98141 | 129
Thin HDMI-cable | 69111 | 229
Raspberry Pi Camera | 87254 | 349
Tempsensor DS18B20 | 87893 | 70
Good Rpi-box with camera mounting holes:
Webhallen, art no 205324 (99 SEK)

## Slide 16: FTP server on RPI
1. sudo apt-get install vsftpd
2. cd /etc
3. sudo nano vsftpd.conf
  local_enable=YES
  write_enable=YES
  chown_uploads=YES
  chown_username=pi
  ftpd_banner=Welcome to xx RPi FTP service!
  => save, exit
4. sudo service vsftpd restart
5. Files are placed in /srv/ftp where pi can read/write
6. Use for instance ”Filezilla” to transfer files

## Slide 17: VNC server on RPI
1. sudo apt-get install x11vnc
2. sudo x11vnc -forver -shared -display :0
3. Create folder ”autostart” in ~/.config
3. Create file named "x11vnc.desktop" in ~/.config/autostart.
4. sudo nano ~/.config/autostart/x11vnc.desktop
  [Desktop Entry]
  Encoding=UTF-8
  Type=Application
  Name=X11VNC
  Exec=x11vnc -forever -shared -display :0
  StartupNotify=false
  Terminal=true
  Hidden=false
  => save, exit
Use for instance ”Real VNC-viewer” to view Rpi desktop remotely

## Slide 18: Rpi gpio pinout
camera
+3.3V
Signal
GND/GND
4.7kΩ

## Slide 19: Temp Sensor DS18B20 on RPI B+
sudo nano /etc/modules
  add "w1-gpio”
  add "w1-therm
sudo nano /boot/config.txt
  add "dtoverlay=w1-gpio,gpiopin=4"

## Slide 20: Temp Sensor DS18B20 on RPI B+
cd /sys/bus/w1/devices/
ls
You will see a listing of the current directory. There should be a directory that is the serial number of your temperature gauge. The serial number of my thermometer 28-0000040be5b6, but every one will be unique. Make a note of yours as you will need it later in step 4. If you have multiple sensors there will be multiple directories listed. If you don't see a directory with lots of numbers and letters like the one above then:
Check your circuit wiring.
Make sure you have the correct resistor (this is very important - yellow, violet, red, gold).
Feel the temperature gauge with your finger. If it feels hot then you have it wired back to front. If you do see the directory then type cd followed by the directory name:
cd 28-0000040be5b6
cat w1_slave
You will now see a dump of the w1_slave file that contains the temperature data in celcius (refer Figure 3). 20812 is 20.812 degrees celcius.

## Slide 21: Temp sensor Python script 1(3)
# A simple sw to log temperature with a Raspberry Pi, with the DS18b20 sensor connected.
# It generates two text-files, one with a time stamp and the temperature every minute
# and a second file with just the latest temperature value.
# The following needs to be done in order to run the script on a RPi B+
# sudo nano /etc/modules
# >add "w1-gpio"
# >add "w1-therm"
# sudo nano /boot/config.txt
# >add "dtoverlay=w1-gpio,gpiopin=4"
import os
import glob
import time
import datetime
#os.system('sudo modprobe w1-gpio') #Needed for Rpi B
#os.system('sudo modprobe w1-therm') #Needed for Rpi B
base_dir = '/sys/bus/w1/devices/'
device_folder = glob.glob(base_dir + '28*')[0]
device_file = device_folder + '/w1_slave'

## Slide 22: Temp sensor Python script 2(3)
def read_temp_raw():
f= open(device_file, 'r')
lines= f.readlines()
f.close()
return lines
def read_temp():
lines = read_temp_raw()
while lines[0].strip()[-3:] != 'YES':
time.sleep(0.2)
lines = read_temp_raw()
equals_pos = lines[1].find('t=')
if equals_pos != -1:
temp_string = lines[1][equals_pos+2:]
temp_c = float(temp_string) / 1000.0
ts = time.time()
st = datetime.datetime.fromtimestamp(ts).strftime('%Y-%m-%d %H:%M:%S')
log_entry=str(st)+' '+str(temp_c)+'\n'
return log_entry

## Slide 23: Temp sensor Python script 3(3)
while True:
ts1=time.time()
temp_log_entry=read_temp()
f = open('TempLog.txt','a')
g = open('TempLastValue.txt','w')
f.write(temp_log_entry)
g.write(temp_log_entry)
g.close()
f.close()
ts2=time.time()
delay=59.91-(ts2-ts1)
time.sleep(delay)

## Slide 24: Camera module
Commands for testing:
”Raspistill –o test.jpg”
”Raspivid –t [time in millisec]”

## Slide 25: Server node shell script example
#!/bin/bash
ip_add_list_file=$1
tempdir=`mktemp -d /var/tmp/LAMOS.pingtest.result.XXX
`date=`date`
while read addr ; do ( ping -c 1 -w 1 $addr > /dev/null 2>&1 ; if [ $? == 0 ] ; then touch $tempdir/$addr ; fi ) & done < $ip_add_list_file
wait
while read addr ; do if [ -e $tempdir/$addr ] ; then echo "$date;Pass;$addr" ; else echo "$date;Fail;$addr" ; fi done < $ip_add_list_file
rm -r $tempdir > /dev/null 2>&1
#Note! Running this on a Rpi might break the SD-card due to too many write-operations!

## Slide 26: Ansible playbook example
From Jose